## Slide 1
TERMS AND CONDITIONS
These PowerPoint slides are a tool for lecturers, and as such:
YOU MAY add content to the slides, delete content from the slides, print out the slides, and save the slides onto your computer or server.
YOU MAY NOT resell, reproduce or redistribute the content in any form whatsoever, without prior written permission from the copyright holder.
© Troupant Publishers (Pty) Ltd, 2016
Selected images used under licence from Shutterstock.com

## Slide 2: Engineering Systems
NQF Level 2

## Slide 3: Engineering systems and their applications
Topic 1

## Slide 4: Electrical systems
Module 1

## Slide 5: VIDEO: Mike Gumbo

## Slide 6: Electrical systems and their components
Unit 1.1

## Slide 7: Basic electrical concepts
Conductors: materials that allow an electric current to pass through them.
Insulators: materials that block the flow of electricity.

## Slide 8: Direct current (DC)
Direct current (DC) is current that flows in one direction only in a circuit.
Example: current supplied in a torch by a battery

## Slide 9: Direct current (DC)
Figure 1.3 Graphic representation of direct current (DC)

## Slide 10: Alternating current (AC)
Alternating current (AC) is current where the direction and amplitude of the current flow changes at regular intervals.
Example: electricity supplied by a power station and supplied to homes.

## Slide 11: Alternating current (AC)
Figure 1.4 Graphic representation of alternating current (AC)

## Slide 12: Basic electrical concepts
Electrical term | Symbol | SI unit
Electric current | I | ampere (A)
Potential difference | pd | volt (V)
Voltage | V | volt (V)
Electromotive force | emf | volt (V)
Resistance | R | ohms (Ω)

## Slide 13: Ohm’s Law
The current flowing in a circuit is directly proportional to the applied voltage across the circuit and inversely proportional to the resistance of the circuit provided that the temperature remains constant.

## Slide 14: Ohm’s Law
Can be rearranged to find voltage or resistance:

## Slide 15: Series circuits
Figure 1.7 Resistors connected in series

## Slide 16: Parallel circuits
Figure 1.8 Resistors connected in parallel

## Slide 17: VIDEO: Series circuits

## Slide 18: Measuring basic electrical quantities
Electrical quantity to be measured | Instrument needed | How to measure
Current | Ammeter | Connect in series
Voltage | Voltmeter | Connect in parallel across load
Resistance | Ohmmeter | Connect in parallel across component
Table 1.1 Measuring basic electrical quantities

## Slide 19: Measuring basic electrical quantities
Electrical quantity to be measured | Instrument needed | How to measure
Current | Ammeter | Connect in series
Figure 1.9 Connecting an ammeter in series in a circuit

## Slide 20
Electrical quantity to be measured | Instrument needed | How to measure
Voltage | Voltmeter | Connect in parallel across load
Figure 1.10 Measuring voltage in a DC circuit

## Slide 21
Electrical quantity to be measured | Instrument needed | How to measure
Resistance | Ohmmeter | Connect in parallel across component
Figure 1.11 Using an ohmmeter

## Slide 22: Multimeter
Figure 1.13 A digital multimeter

## Slide 23: Factors influencing the resistance of a material
Length.
Cross-sectional area.
Resistivity.
Temperature.

## Slide 24: Factors influencing the resistance of a material
Figure 1.15 Conductor 1 will have more resistance than conductor 2
Figure 1.16 The longer the wire is, the greater its resistance is
Length

## Slide 25: Factors influencing the resistance of a material
Cross-sectional area
Figure 1.17 The thicker the wire is, the less its resistance is
Figure 1.18 The inversely proportional relationship between resistance and cross-sectional area

## Slide 26: Factors influencing the resistance of a material
Resistivity
Figure 1.19 Conductor 1 will have more resistance than conductor 2

## Slide 27: Factors influencing the resistance of a material
Temperature
The resistivity and resistance of a material change when temperature changes.
The resistance of most metals increases as their temperature increases.

## Slide 28: Circuit diagrams
A circuit diagram uses symbols to represent all the circuit components and to show how the components are connected in a circuit.
Figure 1.20 A simple circuit diagram

## Slide 29: Table 1.2 Common electrical symbols

## Slide 30: Table 1.2 Common electrical symbols (continued)

## Slide 31: Table 1.2 Common electrical symbols (continued)

## Slide 32: Table 1.2 Common electrical symbols (continued)

## Slide 33: Guidelines for drawing circuit diagrams
Use the correct symbols.
Use a suitable symbol orientation.
Pay attention to the arrangement of symbols on the diagram.
Pay attention to the routing of interconnections.
Make sure your drawing is neat and tidy.

## Slide 34: Lamps in series
Figure 1.22 Two lamps connected in series

## Slide 35: Lamps in parallel
Figure 1.23 Two lamps in parallel

## Slide 36: A bell circuit
Figure 1.25 A bell circuit

## Slide 37: A relay circuit
Figure 1.27 Symbols for a relay

## Slide 38: Control devices for circuits – switches
Switches are used to control an electrical device or system and open and close a circuit.
When the switch is open, the circuit is open and no current can flow.
When the switch is closed, current will flow.

## Slide 39: Switches
Single-pole single-throw (SPST) switch
Figure 1.28 A single-pole single-throw (SPST) switch

## Slide 40: Switches
Single-pole double-throw (SPDT) switch
Figure 1.29 A single-pole double-throw (SPDT) switch

## Slide 41: Switches
Double-pole single-throw (DPST) switch
Figure 1.30 A double-pole single-throw (DPST) switch

## Slide 42: Switches
Double-pole double-throw (DPDT) switch
Figure 1.31 A double-pole double-throw (DPDT) switch

## Slide 43: Push switches or buttons
Two basic types of push or button switches:
Push-to-make switches.
Push-to-break switches.
Figure 1.32 A push-to-make switch

## Slide 44: Push switches or buttons
Push-to-break switches
Multiposition switch
Figure 1.33 A push-to-break switch
Figure 1.34 A multiposition switch

## Slide 45: Contactors
Figure 1.35 A contactor

## Slide 46: Motors
AC motor
DC motor
Figure 1.37 A DC motor
Figure 1.36 An AC motor

## Slide 47: Motors
Figure 1.38 A stepper motor
Stepper motor

## Slide 48: VIDEO: Motor

## Slide 49: Control devices for motors
Simple DC control
Figure 1.39 Simple DC control

## Slide 50: Simple DC control
Reversing the direction of a DC motor.
Figure 1.40 Reversing the direction of a DC motor

## Slide 51
Rotary switches
Figure 1.41 Rotary switches used to control motors

## Slide 52
Manual forward or reverse switches
Figure 1.42 Direct starting on motor
Figure 1.43 Forward or reverse of a motor

## Slide 53: Earthing
Types of electric shocks:
  Direct contact.
  Indirect contact.
Figure 1.45 Direct contact with unearthed electrical equipment

## Slide 54: Circuit protection devices
Purpose of circuit protection devices:
  Prevent damage to the circuit.
  Prevent fires.
  Protect against personal injury.
Two basic forms of electrical faults:
  Short circuits.
  Overload.

## Slide 55: Types of protection devices
Fuses.
Circuit-breakers.
Isolators.
Earth leakage units.

## Slide 56: Types of protection devices
Fuses.
Designed to melt in case of excessive current.
Figure 1.47 Slow-blow fuses

## Slide 57: Types of protection devices
Circuit-breakers.
Devices with preset current limits that operate automatically to protect a circuit.
Figure 1.50 A circuit-breaker

## Slide 58: Types of protection devices
Isolators.
Figure 1.51 An isolator

## Slide 59: Types of protection devices
Earth leakage units.
Figure 1.52 An earth leakage unit

## Slide 60: Plugs
Protective earthing conductor: ends at top pin or largest pin – yellow/green.
Live conductor: ends at the bottom right-hand pin - brown.
Neutral conductor: Ends at the bottom left-hand pin – blue.

## Slide 61: Plugs
Figure 1.53 Terminal arrangement for plugs

## Slide 62: Consequences of wiring a plug incorrectly
It can cause a fire.
There is risk of injury from an electric shock.
Equipment may be damaged.
It can void the warranty of the equipment.

## Slide 63: Summative assessment
Test your knowledge of this section by completing the Summative assessment (page 23 of your Student’s Book)