## Slide 1
TERMS AND CONDITIONS
These PowerPoint slides are a tool for lecturers, and as such:
YOU MAY add content to the slides, delete content from the slides, print out the slides, and save the slides onto your computer or server.
YOU MAY NOT resell, reproduce or redistribute the content in any form whatsoever, without prior written permission from the copyright holder.
© Troupant Publishers (Pty) Ltd, 2016
Selected images used under licence from Shutterstock.com

## Slide 2: Engineering Systems
NQF Level 2

## Slide 3: Pneumatic systems
Module 5

## Slide 4: Pneumatic systems and their components
Unit 5.1

## Slide 5: Pneumatic systems
The branch of science and technology that deals with the study and application of the use of pressurised gas to effect mechanical motion.
Pneumatics uses a compressible gas, usually air.

## Slide 6: Introduction
Figure 5.1 A pneumatic wrench

## Slide 7: Air supply
Air supply at the required pressure, that is dry and clean is needed for effective performance of a pneumatic system.
A compressor is used to generate compressed air.

## Slide 8: VIDEO: Compressor

## Slide 9: Air supply
Use of compressed air:
To determine the status of processors (sensors).
Information processing (processors).
Switching of actuators.
Performing work (actuators).

## Slide 10: Components of a pneumatic system
Compressor.
Air receiver or reservoir.
Air distribution system consisting of:
  Main line.
  Ring lines.
  Air pressure regulators.
  Filters.
  Lubricators.
  Valves.

## Slide 11: Components of a pneumatic system
Air service unit consisting of:
  Air filter.
  Pressure regulator.
  Lubricator.
Valves that perform various functions.
Actuators.
Visual indicating devices.
Pneumatic air lines.

## Slide 12: Compressor
All compressors have the same function, namely to compress air.
The compressor piston draws air through a valve from the atmosphere at atmospheric pressure. Air is compressed.

## Slide 13: Compressor
Figure 5.2 Parts of a compressor

## Slide 14: Air receiver
The function is to provide constant air pressure in a pneumatic system.
The large surface area cools the air and separates moisture in the air, which is removed as water through a drain plug.

## Slide 15: Air distribution system
Air lines consist of a main line and ring lines.
Air pressure regulators are fitted in the air lines to regulate line pressure.
Filters and lubricators are also fitted.

## Slide 16: VIDEO: Drier

## Slide 17
Figure 5.3 A compressed air distribution system
Air distribution system

## Slide 18
Pneumatic air lines include:
Galvanised iron pipes.
Copper pipes.
Rubber hoses.
Plastic and nylon hoses.
Reinforced rubber hoses.
Flexible material hoses.
Air distribution system

## Slide 19: Air service unit
An air service unit prepares the air for use after it has been compressed.
Air service unit consists of the following:
  Air filter.
  Regulator.
  Lubricator.

## Slide 20: Air service unit
Air filter
Figure 5.4 An air filter

## Slide 21
Pressure
regulator
Air service unit
Figure 5.5 A typical pressure regulator

## Slide 22: Valves
The function of valves is to control the pressure or flow rate.

## Slide 23: Valves
Categories of valves:
Directional control valves.
Non-return valves.
Flow control valves.
Pressure control valves.
Shut-off valves.
Emergency stop valves.

## Slide 24: Valves
Directional control valves
Number of ports or openings (ways).
Number of positions.
Methods of actuation of the valve.
Methods of return actuation.

## Slide 25: Directional control valves
Table 5.1 Ports and positions (ways)

## Slide 26: Non-return valves
Valves
Non-return valves allow air to flow through the device in one direction, while blocking the air flow in the opposite direction.

## Slide 27: Flow control valves
Figure 5.6 A flow control valve
Valves

## Slide 28: Valves
Pressure control valves
Pressure relief valves.
Pressure regulating valves.
Pressure sequence valve.

## Slide 29: Valves
Pressure relief valves
  Used to ensure that the receiver pressure is limited for safety and that the supply pressure to the system is set to the correct pressure.

## Slide 30: Valves
Pressure relief valves
Figure 5.7 A pressure relief valve

## Slide 31: VIDEO: Pressure vessel

## Slide 32: Valves
Pressure regulating valves
  Keep the pressure constant, regardless of any pressure fluctuations in the system.

## Slide 33: Valves
Pressure sequence valves
  Used if a pressure-dependent signal is required for the operation of a control system.

## Slide 34: Valves
Shut-off valves
  Pneumatic systems should always be fitted with some form of isolation.
  This allows for maintenance and servicing to take place while the main system is still in use and pressurised.

## Slide 35: Valves
Shut-off valves
Figure 5.8 A stop cock

## Slide 36: Valves
Emergency stop valves
Two types:
A push-operated latching button which requires a twist action to release.
A push-operated valve which requires a key to release.

## Slide 37: Actuators
Actuators convert energy in the form of compressed air into linear or rotary motion.
A pneumatic motor converts pneumatic energy into mechanical rotary motion.

## Slide 38: Actuators
Figure 5.9 A single-acting cylinder

## Slide 39: Actuators
Pneumatic motor characteristics:
Smooth regulation of speed and torque.
Small size (weight).
Overload safe.
Explosion proof.
Requires less maintenance.
Insensitive to dust, water, heat and cold.
Direction of rotation easily reversed.

## Slide 40: Visual indicating devices
They represent the operating status of a pneumatic system visually.
Serve as a primary diagnostic aid.
Include counters, pressure gauges, timers and optical indicators.

## Slide 41: Visual indicating devices
Figure 5.11 A pressure gauge

## Slide 42: Control circuits for cylinders
There are two types of control circuits:
For single-acting cylinders.
For double-acting cylinders.

## Slide 43: Control circuit for a single-acting cylinder
Figure 5.12 Initial position
Figure 5.13 Activating the push button

## Slide 44: Control circuit for a single-acting cylinder
Figure 5.14 Circuit diagram for a single-acting cylinder

## Slide 45: Control circuit for a double-acting cylinder
Figure 5.15 Initial position
Figure 5.16 Activating the push button

## Slide 46: Control circuit for a double-acting cylinder
Figure 5.17 Circuit diagram for a double-acting cylinder

## Slide 47: Pneumatic systems
Advantages | Disadvantages
Air can easily be transported in pipelines, even over long distances. | Leaks are difficult to trace.
Air is freely available all the time. | Pneumatic systems are not suitable for large equipment.
Most components do not require lubrication. | Air carries moisture which condenses and poses a corrosion, contamination and freezing threat to the internal workings of the components and the pipework.
The operating components are of simple construction. | 
Compressed air is a fast-working medium. This enables high working speeds to be attained. | High-pressure air is ‘explosive’ by nature.
Compressed air can be stored in a reservoir and used as required. | 
Advantages and disadvantages of pneumatic systems

## Slide 48: Summative assessment
Test your knowledge of this section by completing the Summative assessment (page 86 of your Student’s Book)